## Slide 1
Estimation of a Normal Process Variance
from Measurements
with Large Round-Off Errors
Diamanta Benson-Karhi, the Open University of Israel Edna Schechtman, Ben-Gurion University

## Slide 2
Measurement Errors
Gertsbakh, I., (2003), Measurement Theory for Engineers, Springer-Verlag, Berlin Heidelberg.
Measurement is the process of
assigning a number to a measurand
which is a random variable.
Measurements are used to estimate the
"true" value of the measurand using
special measuring instrument
and a specified technical procedure.
the "true" value of the measurand
the resulting outcome of the measurement
the deviation of X from its mean value
the pure measurement error
systematic measurement error
Random measurement error

## Slide 3
Round-off Errors
Statistical methods are based on an
assumption that numerical data are
"exact” (infinite number of decimal places).
Measured and archived data are sometimes rounded-off.
Rounding-off may occur due to the characteristics of a measuring instrument or from post-processing of raw data before archival.
Ignorance of the rounding-off can render elementary methods of statistical inference inappropriate and misleading.
Round-off error is typically systematic

## Slide 4
Large Round-off Errors
Measuring instruments have readings
with a discrete scale with step h.
Typically measurement results are rounded-off to the
nearest half of the interval between the adjacent scale marks.
The value of h depends on the measuring instrument's precision.
The desired precision must depend on the spread of the
measurement results in the population.
Special measurements
Regular measurements
Regular estimation procedure
Cochran and Cox, 1957
Gertsbakh, 2003
Modified estimation procedure

## Slide 5
Numerical example – Fetal Femur Length

## Slide 6
Round-Off Errors in Normally Distributed Measurements
the rounded values of the measurand
The measurand
the round-off error
the integer
part of X
Yi takes a maximum
of 5 different values
h0 denotes the mode
Box and Luceno (1997) and Krylov (1950)

## Slide 7
The naïve estimator
Pretends that the observed data are the true values.
Uses the sample variance of the Y’s
to estimate the variance of X.
Numerical Example
Consider h=1, μX=0.5, σX=0.25.
δ=0.25<0.5 YЄ[0,1] with probability 0.5.
For n=5, P(either all 0’s or all 1’s)=2/32
P(4 times 0 and one time 1 or visa versa)=10/32
Variance Point Estimation from Rounded Data
Basic Assumptions:
The round-off error (η) is the only measurement error (Gertsbakh, 2003).
μX is known.

## Slide 8
Sheppard’s Correction (1898)
Popular
Simple
Non-parametric
X and η are independent
Sheppard's correction

## Slide 9
y= y1,y2,…,yn
Maximum Likelihood Estimation (MLE)
Parametric (normal distribution)
Schader and Shmid (1984) and Gertsbakh (2003)
A size-n sample of rounded-off measurements:
The likelihood function of the sample y:
μX is assumed to be known.
Log(L) is unimodal Finding MLE is well defined
More accurate than Sheppard’s correction

## Slide 10
The Calibration Model
Calibration Curve
y = f(x)
measurement
measurand
Calibration Model
Y= f(x)+ε
random variable
zero-mean random variable
E(Y|x)=f(x)
calibration curve
unknown
f(x)
collect preliminary data series (exact known x versus Y)
estimate f(x)
by
we will use this technique in order to estimate based on the observed

## Slide 11
The Calibration Model for Variance Estimation
h, μX
P(Y=y)=f(σX)
δ, h0, μX
calibration function:
polynomial proximity
f(·) is unknown
The polynomial degree
the vector of the polynomial coefficients
finding the
n roots of
the equation

## Slide 12
Simulation
Description

## Slide 13
Results/Bias
n=1000
h=1
h0=3
δ=0.4
δ=0.3
h2/12
δ=0.4
n=100
δ=0.4
n=30

## Slide 14
Results/MSE
μX
μX
μX
Calibration n=1000
Sheppard n=1000
Naïve
n=1000

## Slide 15
n=100
h=10
δ=0.35
h0=100
n=50
h=10
δ=0.35
h0=100

## Slide 16
n=1000
h=10
δ=0.35
h0=100
n=100
h=10
δ=0.5
h0=100

## Slide 17
Conclusions
Calibration/Naïve/Sheppard
The calibration estimator is unbiased.
The calibration estimator is not affected from changes in μX or δ.
Sheppard correction is accurate in for every δ and n.
Sheppard correction is not always better than the naïve estimator.
The calibration model is better than both a-parametric estimators.
Calibration/MLE
In most cases the calibration model and MLE are equally accurate.
The calibration model performs better close to the half point.
The MLE performs better close to the mode.
MLE is more sensitive to changes in the sample size (n).
At the half point MLE usually can’t find any solution.

## Slide 18
Comparison Criteria

## Slide 19
μX=35
h=10
The half point

## Slide 22
The mean and the variance of Y